## Slide 1: Midterm Review 3 – Nov 01
Agenda
  Midterm Review / Practice Questions
    Arduino Programming
    Software Design
    Software Development Environment
    Computer Hardware & Software
  Catch-Up Other Module Work
Upcoming
  TOMORROW: Midterm Test – Written, Individual (33%)
  Friday: Midterm Test – Programming, Individual (33%)
  Monday: Midterm Test – Group (33%)

## Slide 2: Schedule
Yesterday
  Review / Practice: Computer Development & Hardware
Today
  Review / Practice: Software Design & Arduino Programming
Wednesday
  Review / Practice: Arduino Programming
Thursday
  Midterm Test – Written, Individual (33%)
Friday
  Midterm Test – Programming, Individual (33%)
Monday
  Midterm Test – Group (33%)

## Slide 3: Arduino Programming Review
Write a block of computer code defines an integer variable called “blinkTimes” and assigns it an initial value of 6.
int blinkTimes = 6;

## Slide 4: Arduino Programming Review
Write a block of computer code that uses an “if’ statement that checks the value of “blinkTimes” and turns on a LED if the value is less than or equal to 4.
if (blinkTimes <= 4)
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};

## Slide 5: Arduino Programming Review
Modify your “if’ statement to turn on a LED only if the value is greater than 2 or less than or equal to 8.
Add a line comment to your code for question #3 to explain your changes.
// Note: The “or” function in the Arduino C Language
// looks like “||”
if ((blinkTimes > 2) || (blinkTimes <= 8) )
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};

## Slide 6: Arduino Programming Review
Write a block of computer code that uses an “for’ statement that checks the value of “blinkTimes” and blinks a LED the specified number of times.
for (int i = 0; i < blinkTimes; i++)
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};

## Slide 7: Arduino Programming Review
Write a block of computer code that defines a procedure called “blink” that contains computer code to blink a LED.
void blink () {
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};

## Slide 8: Arduino Programming Review
Modify your procedure to add an integer parameter called “times”. Add code to your procedure to use a “for” loop to blink the LED the specified number of “times”.
void blink (int times) {
for (int i = 0; i < times; i++)
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};
};

## Slide 9: Arduino Programming Review
Modify your procedure to add a local integer variable called “threshold” and assign it a value of 3. Add code to your procedure to use an “if” statement to blink the LED only if the specified number of “times” is greater than “threshold”.
void blink (int times) {
int threshold = 3;
if (times > threshold)
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};
};

## Slide 10: Arduino Programming Review
Explain what happens if there is a second variable called “threshold” declared in another part of the program..
void loop () {
int threshold = 6;
blink (5);
Serial.println(threshold);
}
void blink (int times) {
int threshold = 3;
if (times > threshold)
{
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
};
Serial.println(threshold);
};