## Slide 1: Programming Debrief 2 – Nov 09
Agenda
  Continue Discussion: Arduino Fundamentals
  Programming: Midterm Specifications
    Group Assignments
    Apply Arduino Fundamentals
    Complete Program Tomorrow
Upcoming
  By Tomorrow Complete a Working Program

## Slide 2: Group Assignments
Version A (1) | Version B (2) | Version C (3)
Udistan Harry Bikram | Gurnoor Birkaran Daniel Todrique | Manveer Helal Karman Amar
Version A (4) | Version B (5) | Version C (6)
Akashdeep Antonio Puneet | Jujhar Jasman Shemar | Karamvir Javon Brad

## Slide 3: A Basic Arduino Program
// The setup function runs only once when you first start the program
void setup () {
// Initialization code goes here
}
// The loop function runs over and over 20 times a second
void loop () {
// Main program code goes here
}

## Slide 4: Global Variables & Constants
// Global variables and constants are declared at the top of the file
int GREEN_LED = 10;
int RED_LED = 11;
int blinkTimes = 0;
// The setup function runs only once when you first start the program
void setup () {
// Initialization code goes here
}
// The loop function runs over and over 20 times a second
void loop () {
// Main program code goes here
}

## Slide 5: Initialization Code
// The setup function runs only once when you first start the program
void setup () {
// Initialization code goes here
pinMode(GREEN_LED, OUTPUT);
pinMode(RED_LED, OUTPUT);
Serial.begin(9600);
}

## Slide 6: User Defined Procedures
// The "blinkLed" function is a procedure that you can define
// to blink the specified LED colour the specified number of times
void blinkLed (int ledColour, int blinkTimes) {
for (int i = 1; i <= blinkTimes; i++)
{
digitalWrite(ledColour, HIGH);
delay(500);
digitalWrite(ledColour, LOW);
delay(500);
Serial.print("Blink time =");
Serial.println(i);
}
}

## Slide 7: Reading Strings from the Console
// The loop function runs over and over 20 times a second
void loop () {
String typedColour = " ";
int ledNumber = LED_BUILTIN;
Serial.println("Please enter a LED colour.");
// Keep waiting for the user to type something
while(Serial.available() == 0) {
}
// Read what was typed
typedColour = Serial.readString();
}

## Slide 8: Using What Was Typed
// The loop function runs over and over 20 times a second
void loop () {
// Read what was typed
typedColour = Serial.readString();
// Check what the user typed to set the LED colour
if (typedColour == "green") {
ledNumber = GREEN_LED;
Serial.println("The GREEN LED is set.");
}
if (typedColour == "red") {
ledNumber = RED_LED;
Serial.println("The RED LED is set.");
}
// Blink the led 4 times
blinkLed(ledNumber, 4);
}

## Slide 9: Reading Numbers from the Console
// The loop function runs over and over 20 times a second
void loop () {
......
Serial.println("Please enter TIMES to blink.");
// Keep waiting for the user to type something
while(Serilal.available() == 0) {
}
// Read what was typed
blinkTimes = Serial.parseInt();
// Blink the led the requested number of times
blinkLed(ledNumber, blinkTimes);
}

## Slide 10
// Global variables and constants are declared at the top of the file
int GREEN_LED = 10;
int RED_LED = 11;
int blinkTimes = 0;
// The setup function runs only once when you first start the program
void setup () {
// Initialization code goes here
pinMode(GREEN_LED, OUTPUT);
pinMode(RED_LED, OUTPUT);
Serial.begin(9600);
}
// The loop function runs over and over 20 times a second
void loop () {
// Main program code goes here
String typedColour = " ";
int ledNumber = LED_BUILTIN;
Serial.println("Please enter a LED colour.");
// Keep waiting for the user to type something
while(Serial.available() == 0) {
}
// Read what was typed
typedColour = Serial.readString();
// Check what the user typed to set the LED colour
if (typedColour == "green") {
ledNumber = GREEN_LED;
Serial.println("The GREEN LED is set.");
}
if (typedColour == "red") {
ledNumber = RED_LED;
Serial.println("The RED LED is set.");
}
// Blink the led 4 times
blinkLed(ledNumber, 4);
Serial.println("Please enter TIMES to blink.");
// Keep waiting for the user to type something
while(Serial.available() == 0) {
}
// Read what was typed
blinkTimes = Serial.parseInt();
// Blink the led the requested number of times
blinkLed(ledNumber, blinkTimes);
}
// The "blinkLed" function is a procedure that you can define
// to blink the specified LED colour the specified number of times
void blinkLed (int ledColour, int blinkTimes) {
for (int i = 1; i <= blinkTimes; i++)
{
digitalWrite(ledColour, HIGH);
delay(500);
digitalWrite(ledColour, LOW);
delay(500);
Serial.print("Blink time =");
Serial.println(i);
}
}